## Slide 1: The Role of Packaging in Food Sustainability
Daniel McKamy CLEMSON UNIVERSITY
Cooperative Extension
Food Systems and Safety, Extension Associate
Field Operations
511 Westinghouse Road, Pendleton, SC 29670
864.905-7986
www.clemson.edu/extension/food

## Slide 2: Outline
Food Waste Emerges as a Priority
Food Science and Shelf Life
Consumers Attitudes Towards Food Waste
Collaborating to Reduce Food Waste
2

## Slide 3: Estimates of Global Food Waste
Source: Food and Agriculture Organization of the United Nations (2011)
Over one third of the food we produce is never consumed
Cereals
Fruits & Vegetables
Milk
Meat
Fish
37%
58%
18%
40%
23%
Annual Global Food Waste as a % of Production
3

## Slide 4: U.S. Retail and Consumer Food Waste
Source: USDA (2014)
31% of retail food supply goes uneaten, valued at $162 Billion
Weight of Food Loss
Economic Value of Food Loss
Caloric Value of Food Loss
4

## Slide 5: US Fresh Food Sales: Percentage Sold Packaged vs Wasted (%) Euromonitor International, 2017 & ReFED 2016

## Slide 6: Consumer Food Waste Causes
Source: WRAP (2013)
Shelf life of perishable foods is responsible for over 50% of loss
6

## Slide 7: Impacts of Food in the Supply Chain
Greenhouse Gas Contributions
U.S. Poultry Supply Chain
7
Source: AMERIPEN Value of Packaging (2013)
Overall food waste environmental impact can be significant, and occurs after resources have been invested

## Slide 8: Food Science and Shelf Life
8

## Slide 9: What is Food Science?
The study of all aspects of food
  Raw production
  Handling
  Processing
  Packaging
  Distribution
  Final consumption
9

## Slide 10: What Determines Shelf Life?
All quality aspects of the food
  Color
  Texture
  Flavor
  Aroma
  Nutritional Value
  Food Safety
  Food Spoilage
10

## Slide 11: How Do We Extend Shelf Life?
By processing
  Refrigeration
  Freezing
  Canning
  Drying
  Formulation (added salt, sugars, acids)
  Chemical and Physical Sanitation (Blanching, Irradiation)
11
CHEMICAL
SANITIZERS
SANITATION
CHEMICAL
PHYSICAL
HEAT
RADIATION
WET
DRY
UV
G RAY
Non-Food Contact
Food Contact

## Slide 12: How Do We Extend Shelf Life?
By Cleaning and Sanitation
  Follow Hygiene standards (HACCP, USDA, FDA, CODEX, BRC, SQF, IFS, ISO 22000… etc.)
  Proper Cleaning and Sanitation Protocols
  Hygienic Design on Equipment, Building and Facilities
  Personnel and Personal Hygiene Practices
  Non-Food Contact (surfaces) Chemical Sanitation
  Direct Food Contact (Antimicrobial Treatments)
  End-To-End approach (Farm to Retail)
  Internal and External Audits
12

## Slide 13: How Do We Extend Shelf Life?
By Packaging
  Protects and preserves the product
  Improves ease of handling, distribution, and storage
  Means of advertising and labeling
  Extends product shelf-life, reducing waste.
13

## Slide 14: How Do We Extend Shelf Life Through Packaging?
Modified Atmosphere Packaging (MAP)
  - Allows for centralized packaging and distribution
  - Food preservation - extends product shelf-life
    Retards microbial growth
    Delays senescence/ripening of fruits
    Reduces transpiration
    Reduces physical damage
    Slows enzymatic activity
14
Fresh Food Category | Refrigerated Shelf Life (days) | 
 | Non-MAP | MAP
Fresh red meat (low O2) | 2-3 | 21
Fresh pasta | 3 | 60
Lettuce | 2-4 | 14
Cheese | 7 | 180

## Slide 15: How Do We Extend Shelf Life Through Packaging?
Vacuum Packaging
Reduces the volume of air within a package
Usually requires a “barrier” material
Commonly used with Fresh Red Meats
Gas Flushing
Generally, uses a “barrier” material. Produce packaging is an exception.
Typically incorporates a pre-determined mixture of gases to dilute the atmosphere.
15
Packaging is engineered to withstand abuse, provide barrier and make air-tight seals

## Slide 16: How Do We Extend Shelf Life Through Packaging?
Controlled Atmosphere Packaging
Used primarily for bulk storage and gassing
Common in the produce - fruit industry
Passive Packaging
Modification of the atmospheric concentration within a hermetically sealed package
Typical of respiring products such as fruits and vegetables
Active Packaging
Modification of the packaging material with the intent of causing some change in the package environment or packaged product.
Examples include oxygen scavenging, antimicrobials, and pathogen identification systems.
16

## Slide 17: Fresh Red Meat
What are issues with FRM?
  Color changes
  Microbial spoilage
  Rancidity
  Water loss
  Address through O2 and H2O barrier
17
Myoglobin
Oxymyoglobin
Metmyoglobin
Oxidation
Red Meat Color Change

## Slide 18: Fresh Red Meat Barrier Bag
Vacuum packaged
Prevents ingress of oxygen
  - Reduce microbial spoilage
  - Reduce rancidity
  - Protects meat color
Reduces water loss
18

## Slide 19: Fresh Poultry Packaging
Fresh poultry carries bacteria that break down protein and create a strong sulfur odor
  - Shewanella putrefaciens
Packaged in non-barrier structures to allow odors to escape
Hermetically sealed
19

## Slide 20: Fresh Poultry Packaging Bags
Whole birds, Turkey breasts
Breathable/ non-barrier bags
Abuse resistance
High shrink
Hermetically sealed
20

## Slide 21: Smoked and Processed Meats Ribs Example
Abusive product (sharp bones)
Requires good oxygen barrier
Barrier bag provides O2 barrier and abuse resistance
21

## Slide 22: Smoked and Processed Meats Sliced Pepperoni Example
Presence of oxygen causes
  - Discoloration
  - Rancidity
  - Mold growth
  - Flavor changes
Can address by
  - Vacuum package
  MAP + oxygen scavenging sachet
  or oxygen scavenging film
22

## Slide 23: Fresh Produce
Fresh produce respires. It is “alive”.
  - Uses oxygen and gives off carbon dioxide
Packaging must be permeable to allow oxygen to get to the product and carbon dioxide to escape
Packaging must be tailored to the respiration rate of the product
Different products have different respiration rates
23

## Slide 24: Fresh Seafood
Fresh seafood must be packaged in highly permeable material per the FDA (10K oxygen transmission rate).
This allows for safe packaging for distribution and retail display
C. botulinum concern
24

## Slide 25: Food Science and Shelf Life Summary
The shelf life of various foods is determined by their composition, how they are processed and packaged, and how they are stored.
While fresh foods are desirable it is only through processing and packaging that we can extend shelf life, minimize waste, and provide good quality foods to global consumers.
25

## Slide 26
26
Consumer Attitudes Toward Food Waste

## Slide 27: U.S Consumers Attitudes and Behaviors
Source: Harris Poll on Consumer Food Waste (2014)
27

## Slide 28: Consumer Packaging Preference
Source: Harris Poll on Consumer Food Waste (2014)
28

## Slide 29: Consumer Packaging Preference
Source: Harris Poll on Consumer Food Waste (2014)
29

## Slide 30: Likelihood to Reduce Waste
Source: Harris Poll on Consumer Food Waste (2014)
Resealability
Portioning
30

## Slide 31
Collaborating to Reduce Food Waste
31

## Slide 32: Working the Top of the Pyramid
Source Reduction
Reduce the volume of food waste generated
Feed Hungry People
Donate extra food to food banks, soup kitchens and shelters
Feed Animals
Divert food scraps to animal feed
Industrial Uses
Provide food scraps for rendering, digestion and fuel conversion
Composting
Create a nutrient-rich soil amendment
Landfill/ Incineration
Last resort for disposal
Disposal
Recycling
Donation
U.S. EPA Food Waste Hierarchy
Prevention of Food Waste
32

## Slide 33: U.S. Food Waste Partnerships
Collaboration across the supply chain
Benchmarking global initiatives—driving best practices.
New linkages forming between industry, NGO's, government and academia
33

## Slide 34: Conclusions
Food loss and food waste are serious problems affecting all regions of the world.
As the world’s population continues to grow more and more resources will be required to feed everyone. Land, water, fuel, fertilizer, electricity, etc.
Any food loss results in the waste of all upstream inputs, i.e. fuel, fertilizer, pesticides, water, electricity, labor. These inputs have an impact on the environment.
Packaging can reduce food loss and food waste by protecting products, extending shelf life, and providing portion control.
The effects on the environment from packaging are minor compared to the effects caused by food loss, and the associated waste of upstream inputs.
More and better education of the public is needed to facilitate an understanding of the impact each step of the food production supply chain has on the environment.